## Slide 1: Drone
Basics of Autopilot

## Slide 2: DRONE
Dynamic Remotely Operated Navigation Equipment

## Slide 3: Drone Classification
Based on Application
  UAV – Unmanned Aerial Vehicle
  UGV - Unmanned Ground Vehicle
  UWV - Unmanned Water Vehicle

## Slide 4: Drone Classification
Based on weight and Altitude
Size | Weight ( in kg) | Altitude (ft)
Nano | .25 | 1,200
Micro | .25 - 2 | 3,500
Small | 2 - 25 | < 18,000
Medium | 25 – 150 | < 18,000
Large | >150 | > 18,000

## Slide 5: Autopilot
Pilot Assistance System
User Dependent
Is a advanced Flight Controller

## Slide 6: Types of GCS
Ardu Pilot – windows and mac
Q Ground control – all platforms
APM Planner- Windows, Mac and Linux
MAVProxy- Linux
UgCS
Dev platform – Dronekit.io

## Slide 7: Autopilots available in market
APM – ArduPilot Mega
Pixhawk
Naza MLite
Naza V2
Wookong

## Slide 8: PixHawk
Sensors
  3 Axis - Gyroscope
  3 Axis - Magnetometer
  3 Axis - Accelerometer
  Barometer
Microprocessor
  168 MHz/256KB RAM / 2MB Flash
  32-bit STM32F427 Cortex® M4 core with FPU
  32 bit STM32F103 failsafe co-processor

## Slide 9: Pixhwak Pinout
Spektrum DSM receiver
Telemetry (on-screen display)
Telemetry (radio telemetry)
USB
SPI (serial peripheral interface) bus
Power Module
Safety switch button
Buzzer
Serial
GPS module
CAN ( Controller area network) bus
I2C Splitter or compass module
Analog to digital converter 6.6V
Analog to digital converter 3.3V
LED indicator

## Slide 10: Pixhawk Pinout
Radio Control Receiver Input
S.Bus Output
Main Outputs
Auxiliary Outputs
Input/output Reset Button
SD Card
Flight Management Reset Button
Micro-USB Port

## Slide 11: Pixhawk Pinout
Flight management unit (FMU) power
FMU bootloader mode(flashing) or error (solid)
Input/output unit power
I/O bootloader mode(flashing) or error(solid)
Activity (flashing indicates all units responsive)

## Slide 12: Components of Autopilot System

## Slide 13: Components used
Autopilot ( Flight Controller)
GPS
Telemetry (Air and Ground)
Power Module
PPM encoder, Buzzer, Switch, etc. (optional)

## Slide 14: GPS – Global Positioning System
Working – Trilateration
HDOP – Horizontal Dilution of Precision
Number of satellites – at least 6 but 10 is good

## Slide 15: Flight Modes in Autopilot
Stabilize
Auto
Alt Hold
Position Hold
Loiter
RTL – Return to Launch

## Slide 16: Drone regulations in India
UIN-Unique Identification Number Costs Rs.1000.
UAOP(Unmanned Aerial Operator Permit) –Costs Rs.25000 above 200 feet(60m) ,validity 5 years renew (10,000)
UAOP and UIN not required for Micro and Nano(if operating in enclosed area)

## Slide 17: Equipment requirements
GNSS (Global Navigation Satellite System)
RTL(Return To Launch)
Anti-Collision Strobe lights
NPNT for app based real-time tracking
Fire resistant UIN (unique identification number) plate
Flight data logging capability
Detect and avoid

## Slide 18: Eligibility to get license
18 years
At least Class 10 English
DGCA approved FTO